## Slide 1: Ready for the Midterm?

## Slide 2
Compute the following addition in binary representation where the second addend is 0011:
-0.25 + 0.375
1110 (carry)
1110
+ 0011
0001
0.125

## Slide 3
Compute the following binary multiplication where multiplicand and multiplier are represented using 4 bits:
13 x 14
182
 |  |  |  | 1 | 1 | 0 | 1
 |  |  |  | 1 | 1 | 1 | 0
 |  |  |  | 0 | 0 | 0 | 0
 |  |  | 1 | 1 | 0 | 1 | 
 |  | 1 | 1 | 0 | 1 |  | 
 | 1 | 1 | 0 | 1 |  |  | 
1 | 0 | 1 | 1 | 0 | 1 | 1 | 0

## Slide 4
int function(int a)
{
return 3*a+5;
}
int main()
{
int x=5;
int y;
y = function(x);
...

## Slide 5
fun: # This function overwrites $s0 and $s1
addi $sp, $sp, –8 # adjust stack to make room for 2 items
sw $s1, 4($sp) # save register $t0 for use afterwards
sw $s0, 0($sp) # save register $s0 for use afterwards
li $s0, 3
mul $s1,$s0,$a0 # s1 = 3*$a0 (3*a)
addi $s1,$s1,5 # 3*a+5
add $v0,$s1, $zero
lw $s0, 0($sp) # restore register $s0 for caller
lw $s1, 4($sp) # restore register $t0 for caller
addi $sp,$sp,8 # adjust stack to delete 3 items
jr $ra # Jump to addr stored in $ra
main: # x is $s0, y is $s1
add $a0, $s0, $zero # Argument 1: x ($s0)
jal fun # Save current PC in $ra, and jump to fun
add $s1, $v0, $zero # Return value saved in $v0. This is y ($s1)

## Slide 6
Write MIPS assembly code that compute this expression:
B[3] = a + B[7]
  assume that the base address of the array B is in $s1, 'a' is assigned to $s0, and assume that each array element accessed is in word size.
lw $t0, 28($s1) #B[7]
add $t0, $s0, $t0 #a+B[7]
sw $t0, 12($s1) #a+B[7] -> B[3]

## Slide 7
Write the MIPS assembly code that isolate the first 4 bits of the value contained in register $s1
andi $t0, $s1, 15
#1510 = 11112, isolated 1st 4 bits are stored in $t0

## Slide 8
If these registers contain:
$t0 = 410
$t1 = 210
What is the value of $t2 after this instruction?
sll $t2, $t0, 4
, and thus $t2

## Slide 9
If these registers contain:
$t0 = 410
$t1 = 210
Starting from the values above, what is the value of $t2 after this instruction?
or $t2, $t2, $t1
64= 0100 00002
2= 0000 00102
$t2 is 0100 00102 =66

## Slide 10
For the MIPS assembly instructions below, what is the corresponding C statement?
  Assume that the variables f, g, h, i, and j are assigned to registers $s0, $s1, $s2, $s3, and $s4, respectively.
  Assume that the base address of the arrays A and B are in registers $s6 and $s7, respectively.
  sll $t0, $s0, 2 # $t0 = f * 4 add $t0, $s6, $t0 # $t0 = &A[f] sll $t1, $s1, 2 # $t1 = g * 4 add $t1, $s7, $t1 # $t1 = &B[g] lw $s0, 0($t0) # f = A[f] addi $t2, $t0, 4 lw $t0, 0($t2) add $t0, $t0, $s0 sw $t0, 0($t1)
B[g] = A[f] + A[f+1]

## Slide 11
Which is the two's complement representation of the number -23 ?
11111111111111111111111111101001
11111111111111111111111111101111
11111111111111111111111111111001
11111111111111111111111111101000

## Slide 12
Can you use a NAND port to obtan the same behavior as an inverter?

## Slide 15
This gate outputs 1 if either input is 1 but not both (that is, it outputs 1 if the inputs are different)
Notes: XOR

## Slide 16
Notes: This is a one bit fulladder, try to recreate the truth table